## Slide 1
ARDUINO-BASED AUTOMATION & MULTI-SENSOR MONITORING
SMART SEWAGE INSPECTION AND CLEANING ROBOT
SENSE. MOVE. CLEAN.
An autonomous compact crawler engineered for hazardous pipe inspection, obstacle detection, and active rotary surface scrubbing.

## Slide 2
OPERATIONAL SEQUENCE
MAKING CLEANING SMARTER
An integrated prototype exploring automated, water-assisted sewage inspection and cleaning.
01
MOVEMENT
Tracked chassis navigates uneven pipe terrain.
02
DISTANCE SENSING
Ultrasonic pings detect forward obstacles continuously.
03
WATER DELIVERY
Submersible pump directs pressurized flow to deposits.
04
ROTATING MOP
Front-mounted head scrubs internal pipe walls.

## Slide 3
HARDWARE ARCHITECTURE
SIX KEY COMPONENTS
Arduino Uno
Central microcontroller running logic loops and threshold arbitration.
L298N Motor Driver
High-current dual H-bridge driving tracked gear motors.
HC-SR04 Ultrasonic
Front sonar measuring target proximity and blockage distance.
YF-S201 Flow Sensor
Hall-effect rotor detecting line pressure and water-flow pulses.
MQ-135 Gas Sensor
Air-quality sensing element providing raw analog conduit readings.
Relay & Water Pump
Switched high-load relay actuating 12V water delivery on demand.

## Slide 4
SYSTEM ARCHITECTURE
HOW THE SYSTEM THINKS
Distinct control channels separate autonomous obstacle triggers from passive environmental telemetry.

## Slide 5
DECISION BOUNDARY
THE 15 CM THRESHOLD
Ultrasonic distance dictates system actuation. Any ambiguous reading immediately triggers an automated safety stop.
TARGET IN RANGE
≤ 15 cm
STATE A: ACTIVE CLEANING
Forward Movement: Commanded
Water Pump: Switched ON
Mop Head: Active rotary scrub
TARGET CLEARED / OUT OF RANGE
> 15 cm
STATE B: SAFE STANDBY
Chassis Motors: Commanded STOP
Water Pump: Switched OFF
Fail-Safe: Invalid distance readings default directly to OFF

## Slide 6
SCRUBBING MECHANISM
WATER + ROTATING MOP
The pump supplies water while the rotating front mop helps wipe and clean.
Pump
Water tubing
Water delivery →
Front rotating mop
Mop rotation ↻

## Slide 7
DIAGNOSTICS & TELEMETRY
REAL-TIME OBSERVATION
SERIAL MONITOR
Distance (cm)
Flow rate (L/min)
MQ-135 raw reading
Mode / relay status
Illustrative interface
COMMAND FLAGS
F = Forward
B = Backward
S = Stop
A = Automatic mode

## Slide 8
PROJECT CONCLUSION
FROM IDEA TO WORKING PROTOTYPE
SENSE. MOVE. CLEAN.
Combining electronics, programming, and mechanical design to explore smarter sewage inspection and cleaning through automation.